## Slide 1
Performance Engineering for Red Hat OpenShift Enterprise Workloads: From Architecture to Continuous Optimization
Rani Bharti, Performance Analyst (ranis.bharti@in.ibm.com), IBM,
Infrastructure, Bengaluru
Vivek Koul, OpenShift SME (vkoul@redhat.com), RedHat, Mumbai
Bangalore Performance and Scale Meetup - 2026

## Slide 2
Topics
End-to-End System Architecture Stack: OpenShift on IBM Z
Red Hat OpenShift on IBM Z & LinuxONE: Why OpenShift
Client Case Study – Performance Engineering & IFL Optimization
Target Recommendations & Performance Optimization
XY3 Prod OpenShift — LPAR Isolation Redesign
Why Restructuring & Isolation is Recommended
Bangalore Performance and Scale Meetup - 2026

## Slide 3
FOUNDATION & SYSTEM ARCHITECTURE
End-to-End System Architecture Stack: OpenShift on IBM Z
APPLICATION LAYER
Containerized Enterprise Workloads
• Core Microservices (Payments, Accounts, Risk) • Cloud-Native Ingress & Service Mesh • High-Density Pod Packing
PLATFORM & STORAGE
Red Hat OpenShift Container Platform & ODF Storage
• Dedicated Cluster Pools (Primary & Secondary clusters) • ODF Storage Isolation • Tuned Prometheus (Minimal Profile & 3d Retention)
OPERATING SYSTEM
Red Hat Enterprise Linux (RHEL CoreOS on IBM Z)
• Enterprise Linux Guests • vCPU-to-IFL Scheduling & Topology • Ultra-Fast HiperSockets Colocation with Core Banking
HARDWARE, LPAR & HYPERVISOR
IBM z/VM Hypervisor & IBM zSystems / LinuxONE Hardware
• Dedicated Hardware LPAR Pools • Physical IFL Core Allocation • Full-Stack Telemetry (PerfKit • SAR • MONWRITE • hyptop)
🔍 End-to-End Performance Engineering Methodology:
Correlating metrics across Kubernetes Pods ⟷ Linux OS ⟷ z/VM Hypervisor ⟷ IBM Z Hardware to isolate infrastructure overhead, eliminate CPU steal time, and enable predictable IFL capacity planning for enterprise banking systems.
💡 Architectural Foundation: Each layer in the OpenShift-on-IBM Z stack introduces unique scheduling and virtualization telemetry. Performance engineering ensures that hardware-level IFL efficiency is maintained across all virtualized guests and microservices tiers.
Bangalore Performance and Scale Meetup - 2026

## Slide 4
FOUNDATION & PLATFORM VALUE
Red Hat OpenShift on IBM Z & LinuxONE: Why OpenShift?
Empowering enterprise workloads with cloud-native agility, premier security, and mainframe-grade efficiency
CLOUD-NATIVE AGILITY
Modernize at Scale
• Declarative Operations:
Full-stack Kubernetes automation with built-in Operators & GitOps.
• Microservices Architecture:
Modernize monolithic application into agile, scalable container services.
• Developer Experience:
Consistent self-service developer workflows across hybrid cloud tiers.
COMPUTE DENSITY
Extreme IFL Consolidation
• High-Density Packing:
Run thousands of enterprise pods on dense IFL cores with massive RAM.
• Hypervisor Flexibility:
Flexible deployments across IBM z/VM or RHEL KVM micro-partitions.
• Optimal TCO:
Substantially reduces data center footprint, cabling, power, and software licensing.
ENTERPRISE SECURITY & RESILIENCE
Mission-Critical Trust
• Pervasive Encryption:
Hardware-accelerated cryptographic protection on-chip (CPACF & Crypto Express).
• Five-Nines Availability:
Unmatched fault tolerance, high-availability control plane, & DR (Primary / Secondary Cluster).
• Multi-Tenant Isolation:
Robust hardware-enforced LPAR boundaries and security controls.
SUB-MILLISECOND LATENCY
Core Banking Colocation
• Transactional Proximity:
Co-locate containerized microservices directly with core banking (z/OS, CICS, Db2).
• Ultra-Fast HiperSockets:
Direct memory communication across LPARs without external network switches.
• Real-Time Processing:
Accelerate high-frequency payments and real-time core banking transactions.
Why Performance Engineering on OpenShift on IBM Z Matters
• Multi-Layer Reality: Applications run atop OpenShift Pods ⟷ Linux Guests ⟷ Hypervisor (zvm/kvm) ⟷ Physical IFL Hardware.
• The Need: Without cross-layer telemetry, platform overhead (storage, monitoring, steal time) can mask as high IFL usage.
• The Solution: This study establishes an end-to-end performance methodology to unlock maximum density and peak enterprise efficiency.
Bangalore Performance and Scale Meetup - 2026

## Slide 5
BUSINESS CHALLENGE
High IFL utilization despite low OpenShift workload, creating an IFL utilization mismatch.
High IFL-to-vcpu ratio and IFL contention
CPU steal time
High platform, storage, and monitoring overhead
Shared LPARs across production clusters (Primary & Secondary Cluster)
Unexplained IFL consumption increased capacity pressure, infrastructure cost, and sizing uncertainty.
SOLUTION OVERVIEW
Cross-layer analysis of LPAR, OpenShift, and z/VM metrics to pinpoint IFL consumption.
Correlated workload and infrastructure utilization
Identified major IFL consumers
Quantified IFL usage and optimized sizing
Delivered architecture and configuration recommendations
Technologies / logs: OpenShift • z/VM • Monwrite/Perfkit (z/VM) • SAR • hyptop • Prometheus
INNOVATION HIGHLIGHTS
Differentiator: Cross-layer correlation revealed the hidden causes of high IFL utilization.
Novel Approach: Combined LPAR + OpenShift + z/VM telemetry to isolate infrastructure overhead.
Standout Value: Turned “high IFL, low OpenShift CPU” into clear root causes and actionable recommendations.
BUSINESS IMPACT & METRICS
KEY KPIs
Faster root-cause identification through unified cross-layer analysis
Enables right-sizing and reduces unnecessary IFL/capacity consumption
Reduces CPU contention, steal time, and infrastructure bottlenecks
Clear optimization roadmap for improved OpenShift performance and capacity planning
Key measured finding: Worker processor utilization was 5 times lower than cluster level utilization (e.g Worker ~2IFLs while Cluster ~11IFLs), revealing significant platform/infrastructure overhead.
BEFORE → AFTER
BEFORE: Shared LPARs • High IFL usage • CPU contention • Sizing uncertainty
AFTER: Dedicated LPAR Pools • Root causes identified • IFL usage quantified • Optimized sizing
REUSABILITY / SCALE
Applicable across OpenShift-on-z/VM environments for standardized sizing and optimization.
BASELINE SHARED ARCHITECTURE TOPOLOGY
FUTURE ROADMAP
Automate continuous cross-layer monitoring and anomaly detection.
Enable predictive capacity planning and proactive resource optimization.
EXECUTIVE SUMMARY & INNOVATION DASHBOARD
Client Case Study – Performance Engineering & IFL Optimization
Bangalore Performance and Scale Meetup - 2026

## Slide 6
ARCHITECTURE & CONTINUOUS OPTIMIZATION
Target Recommendations & Performance Optimization
Key architectural restructuring, observability tuning, and runtime modernization for enterprise banking workloads
1. CLUSTER ISOLATION
Separate Production LPAR Pools
• Baseline Topology: Primary Cluster & Secondary Cluster co-located on same LPARs.
• Risk: Cross-cluster contention & maintenance blast radius.
• Recommendation: Deploy clusters on dedicated LPAR sets (e.g. XY3Z141–143 for Primary Cluster, XY3Z151–153 for Secondary Cluster).
• Outcome: Complete workload isolation & zero noisy-neighbor impact.
2. STORAGE (ODF) ISOLATION
Dedicated LPARs for ODF Storage
• Baseline Topology: ODF storage co-located with compute/control nodes.
• Risk: High I/O and storage CPU starve Master/Infra components.
• Recommendation: Split Storage/ODF nodes onto dedicated LPAR pools (e.g. Dedicated Storage LPARs XY3Z147–149 / XY3Z157–159).
• Outcome: Protects control-plane stability & simplifies storage scaling.
3. PROMETHEUS TUNING
Profile: Minimal & 3d Retention
• Retention: Cut default 14-day retention down to 3 days.
• Collection Profile: Set collectionProfiles: minimal in config map.
• Impact: Prometheus captures only essential alert, telemetry & dashboard metrics.
• Outcome: Drastically reduces platform CPU & storage IFL overhead.
4. PLATFORM MODERNIZATION
Upgrade OpenShift from 4.16.x
• Current Version: OpenShift Container Platform 4.16.x.
• Recommendation: Upgrade to latest supported OpenShift release (4.18+ / 4.22).
• Benefits: Improved kernel efficiency on IBM Z, streamlined control-plane footprint, and native performance enhancements.
5. CONTINUOUS OBSERVABILITY
Cross-Layer Monitoring Tools
• Telemetry Stack: Monwrite/Perfkit (z/VM) • SAR • hyptop • Prometheus.
• Proactive Detection: Continuously monitor CPU steal time & hypervisor dispatch delays.
• Early Detection: Identify platform & IFL utilization bottlenecks before production impact.
Bangalore Performance and Scale Meetup - 2026

## Slide 7: XY3 Prod OpenShift — LPAR Isolation Redesign
Current shared-LPAR model vs. recommended isolated-LPAR model with dedicated ODF
Today: shared LPARs
Primary and Secondary run on the same three LPARs, XY3Z141 to XY3Z143.
Proposed: isolated LPARs
Each cluster gets its own dedicated LPARs; Secondary is separate from Primary.
ODF on dedicated LPARs
Storage nodes move to dedicated ODF storage LPARs in both clusters.
Existing Deployment Vs Recommended Deployment
Bangalore Performance and Scale Meetup - 2026

## Slide 8
INFRASTRUCTURE RESTRUCTURING RATIONALE
Why Restructuring & Isolation is Recommended
Eliminating cross-cluster blast radius, protecting control-plane stability, and planning predictable capacity growth
1. CLUSTER ISOLATION
Eliminating Blast Radius
• Co-Location Risk:
Primary Cluster and Secondary Cluster currently run on shared LPARs (XY3Z141–143).
• Fault Propagation:
A resource spike, LPAR-level issue, or maintenance event on one cluster directly impairs the other.
• Dedicated Pools:
Moving to separate LPAR pools (XY3Z141–143 for Primary, XY3Z151–153 for Secondary Cluster) guarantees zero cross-cluster contention.
2. ODF STORAGE ISOLATION
Protecting Control Plane
• Heavy I/O Footprint:
ODF storage workloads are highly I/O and CPU intensive on IBM Z.
• Starvation Risk:
Co-locating storage nodes with Master/Infra components creates severe CPU steal time & starvation.
• Dedicated Storage LPARs:
Splitting ODF onto dedicated Storage LPARs (XY3Z147–149 / XY3Z157–159) ensures control plane resilience & unconstrained storage scaling.
💡 Key Architectural Takeaway: Moving from shared infrastructure to dedicated LPAR tiers eliminates IFL contention and steal time, providing predictable OpenShift performance and isolated failure domains for mission-critical enterprise operations. Successful implementation requires active cross-team collaboration across Mainframe Systems, Linux OS, Storage, and OpenShift Platform teams.
Bangalore Performance and Scale Meetup - 2026

## Slide 9
Thank you !
Q & A